## Slide 1: OCSP Guidelines January 14-16, 2013 Rome, Italy
Notes: <number>

## Slide 2: Why OCSP for Grid
Should be less error-prone than fetch-crl
  when supported in software
  since many fetch-crl issues come from site config trouble
  and CRL downloads are also a ‘DoS’ against CAs
Gives support for dynamicly-inserted sub-CAs
  no advance knowledge needed of all CRL CDPs
  when used in conjunction with new namespaces
  should enable dynamic sub-CA support
Is more timely than CRLs
  cached 6-24 hours, which is ‘reasonable’
  but in many cases (web!) CRL is not retrieved at all!

## Slide 3: OCSP styles
Full-blown real time OCSP (RFC2560)
  Provides protection against replay attack
  Using nonce supplied by client
  Is computed and signed in real-time
  Lots of inbound data so needs HTTP POST
Light-weight OCSP (RFC5019)
  Aim is to be cachable (and stapleable)
  Prefer HTTP GET
  No-nonces (in reply)
  Cacheable, with HTTP headers set according to response
  Does not contain dynamic data, so can be replayed (and thus needs short ‘life time’)

## Slide 4: Light-weight OCSP
RFC5019 leaves some deployment options open
  Choices can be ‘good’ or ‘bad’
  CA has to decide on how to generate responses
  Mistakes by CA in settings can easily lead to DDoS 
  Mistakes by RPs in settings can easily lead to DDoS 
Implementations
  Mixed quality, many implementation miss out on spec: some minor (uses GET even for large requests), or major (always use POST, so response cannot be cached)
  ‘stapling’ RFC 6066 is not widely supported seemingly apache and nginx only
  Even standard OCSP not fully supported by Griddy MW but it acively worked on, and our guidance appreciated

## Slide 5: Impact on CAs
For now, it adds network load to the CA
  Since we do not expect CRL retrieval to stop immediately
  At least one OCSP request will be sent for each service access
The OCSP load is related to the ‘popularity’
  the (subscriber base) of the CA
  how ‘active’ the subscribers are
OCSP request/response is relatively small
  Not that many bytes
  But a lot of requests
OCSP is a critical service (use a HA setup)

## Slide 6: Progressing with OCSP
Guidance for Cas
  Some Cas (DigiCert, TCS/Comodo) already have this
  Few others are almost ready, with RFC5019 or 2560, e.g. CESNET
  But a lot are waiting – would profit from guidance: deployment scenarios, software tooling
Guidance for RPs and developers
  ‘proper’ OCSP clients and RFC5019 not really there
  Profile on ‘expected responses’ helps a lot for coding
  Practical examples to help interpret RFC5019
  Deployment scenarios to make sure RPs don’t DoS us!

## Slide 7: OGF CAOPS-WG & IGTF Documents
Propose two documents
For CAs:
  profile of RFC5019 and expected response content
  deployment suggestions (pre-computed, no/simple VA)
  Software hints for good HTTP headers
  …
For RPs:
  Software development guidance on app-level caching
  Fall-back to CRLs
  Sane cache time default
  Deployment guidance on (squid) caching services
  …